## Slide 1
CHALLENGE: SOVEREIGN TECHNOLOGY FOR INDIA · TRACK 03 — DEFENSE & STRATEGIC TECH
ANTARIKSHA- RAKSHA
A locally-run SSA decision-support console for India's satellites.
Screens protected assets for close approaches and proximity patterns with SGP4, estimates risk with a simplified analytic Pc indicator, and drafts briefs with a local AI model — every decision made by a human, audited.
Local AI
Zero license fees
Offline after TLE fetch
Open-source components
Runs on one laptop — today
Working prototype ·
Public submission repository — code available for evaluation
Notes: Open with the one-line identity: a locally-run SSA decision-support console, working today as a research prototype, built for the Sovereign Technology for India challenge, Track 03. Emphasize: one laptop, local AI, a human makes every decision. Built on open-source components and a local open-weight model; the project repository itself is private and available for evaluation. Say clearly it is not an operational collision-warning service. Positioning: defence-relevant Space Domain Awareness and conjunction-assessment decision support — a research/demo prototype, not a weapon, defence or command system.

## Slide 2
◤ PROBLEM STATEMENT · 1 / 2
ANTARIKSHA-RAKSHA · 02 / 12
India's most critical infrastructure isn't on the ground
▸
India's satellite fleet underpins daily national life — NavIC positioning, GSAT defense communications, Cartosat/RISAT border surveillance and disaster response.
▸
They fly among ~40,000 tracked objects (ESA, 2025); ~2,700 satellites were launched in 2024 (SIA), mostly for large constellations.
▸
Collisions can cascade: debris from the 2007 Fengyun-1C ASAT test and the 2009 Iridium–Cosmos collision still occupies orbits used by Indian EO satellites.
▸
Rendezvous and proximity operations near other spacecraft are publicly reported worldwide — sustained proximity merits human review, without inferring intent.
THE STAKES PER ASSET
High-value assets
Each satellite is a major national investment — plus navigation, banking-timestamp and cyclone-warning services no rupee figure captures.
THE ORBITAL COMMONS
LEO is a finite natural resource. Avoiding debris-generating collisions helps keep orbits usable for future Indian missions.
Notes: Frame the stakes: India's satellite fleet underpins daily national life. About 40,000 objects are tracked (ESA Space Environment Report 2025, 1 Apr 2025: 'About 40 000 objects are now tracked... about 11 000 active payloads'), and about 2,700 satellites were launched in 2024 (Satellite Industry Association, State of the Satellite Industry Report 2025: 2,695 satellites; McDowell counts 2,857 payloads), mostly for large constellations. Collisions can cascade. Proximity operations are publicly reported worldwide and merit human review, without inferring intent. Keep the asset-value framing qualitative.

## Slide 3
◤ PROBLEM STATEMENT · 2 / 2
ANTARIKSHA-RAKSHA · 03 / 12
The decision-support gap in space situational awareness
01 · CONTEXT
India already has SSA capability — ISRO's IS4OM and the NETRA programme build sensing and cataloguing. This prototype explores a complementary, operator-facing decision-support layer — not a replacement, and not integrated with them.
02 · COMMERCIAL LANDSCAPE
Leading commercial SSA services are delivered as cloud services with proprietary models (free and paid tiers exist).
03 · WHAT INDIA NEEDS
An auditable, affordable, locally-run screening and decision-support layer an authorized operator can run — offline after the first data download — with a human in command of every decision.
That is what we prototyped.
Not an operational system.
Notes: Context, stated neutrally: India already has SSA capability (ISRO IS4OM, NETRA). This prototype explores a complementary, operator-facing decision-support layer that is auditable and runs locally. It is not integrated with those programmes or any government system, and is a research prototype, not an operational system. Commercial landscape: leading commercial SSA services (for example LeoLabs) are delivered as cloud services with proprietary models; free and paid tiers exist (for example Slingshot Beacon).

## Slide 4
◤ SOLUTION
ANTARIKSHA-RAKSHA · 04 / 12
Perceive → Reason → Execute, with a human at the trigger
01
PERCEIVE
Public orbital data (CelesTrak GP/TLE) for Indian assets, debris, other active satellites.
Offline TLE cache: runs without network after first fetch.
SGP4 propagation of every orbit on a shared time grid.
02
REASON
Screening (10 km) + refined TCA + simplified analytic Pc indicator — NOT an operational covariance-based Pc.
Proximity-pattern dwell detection (25 km watch, approach geometry).
Criticality-weighted priority: Tier 1 strategic → Tier 3 civil.
Local LLM drafts each brief; a deterministic fact check plus a same-model second pass check it (not independent validation); template fallback if AI is down.
03
EXECUTE
HUMAN-GATED
Operator sees brief, numbers, separation chart, illustrative Δv estimate (not a maneuver plan or recommendation) — then approves, acknowledges or dismisses with a reason.
Rejection reasons feed future prompts (no model training).
Prototype RBAC: only OPERATOR+ can decide; audit records user + role. Optional Telegram alerts.
Nothing is autonomous at the decision point — decision-support only: there is no command path to any spacecraft.
Notes: Walk the three stages: Perceive (public CelesTrak GP data, offline cache, SGP4), Reason (10 km prototype candidate-screening threshold, not a collision criterion; refined TCA; a simplified analytic collision-probability indicator, NOT an operational covariance-based Pc; proximity dwell detection; local LLM brief checked by a deterministic fact check plus a second pass by the same model, not independent validation), Execute (human approves, acknowledges or dismisses with a reason; the illustrative delta-v estimate is not a maneuver plan or recommendation; persistent decision audit; optional Telegram). Land: decision-support only, no command path to any spacecraft. Prototype role-based access is enforced by the backend: only an OPERATOR (or higher) account can record a decision, and each decision stores the acting user and role. Local accounts only, no MFA or SSO; production would need enterprise identity integration.

## Slide 5
◤ WORKING SYSTEM
ANTARIKSHA-RAKSHA · 05 / 12
Built. Tested. Running on a consumer laptop.
CONSOLE SCREENSHOT · LIVE DATA · 2 OCT 2026
< 1 s
PROPAGATE + SCREEN SINGLE LOCAL RUN · 2 OCT 2026
103
OBJECTS INGESTED FROM CELESTRAK · 2 OCT 2026
775
AUTOMATED TESTS PASSED 613 BACKEND + 162 UI · 5 OCT 2026
Human
ALL DECISIONS ARE MADE BY A HUMAN — BY DESIGN
Full-screen 3D console: time-lapse globe with SGP4-propagated tracks, priority-ranked event feed, per-event drawer with AI brief and one-click decisions · LIVE / CACHED / DEMO data-mode labels · separation-profile chart, TLE confidence, CSV + Word/PDF incident export · 11-language UI · labelled controlled demo scenarios, clearly marked DEMO.
STACK Python · FastAPI · SQLite · skyfield/SGP4 · NumPy/SciPy · React · CesiumJS · Ollama (llama3.2) — open-source software + open-weight model, no paid API keys.
Notes: Proof slide. The screenshot is the real console running on live CelesTrak data on 2 Oct 2026: LIVE DATA panel, globe with SGP4-propagated tracks, asset list. Metrics are single local runs on the demo laptop on 2 Oct 2026: 103 objects ingested from CelesTrak (11 Indian assets, 80 debris, 12 other active satellites), propagation + screening under 1 s (0.18 s + 0.16 s), 775 automated tests passed (613 backend + 162 frontend, 3 Oct 2026). All decisions are made by a human, by design. Any demo event is a labelled controlled scenario.

## Slide 6
◤ TECHNOLOGY DIFFERENTIATION · 1 / 2
ANTARIKSHA-RAKSHA · 06 / 12
A transparent, guard-railed LLM brief pipeline
Drafter + consistency check
A local LLM writes each brief from the computed numbers; a deterministic fact check and a second pass of the same model check the draft against them — not independent validation. Flagged twice → the human sees the flag, not a hidden failure.
Provenance on every output
Each brief is chip-labeled: AI-drafted + consistency status , or deterministic template. The operator always knows what produced what they are reading.
In-context feedback — honestly
Operator rejection reasons are added to future prompts (in-context feedback). We say exactly that — no model weights change: no training, fine-tuning or RL. It is prompt context, not learning.
Never blocks; numbers from code
Ollama down → deterministic template brief + degraded-mode banner. Prompts forbid invented numbers and intent speculation; displayed numbers come from the backend — proximity language stays factual and neutral.
Notes: AI design, stated plainly: the local LLM drafts a brief from computed numbers; a deterministic fact check plus a second pass of the same model check consistency (not independent validation); every brief is labelled; rejection reasons are prompt context only, with no model weights changed (no training, fine-tuning or RL); if the LLM is down, a deterministic template takes over.

## Slide 7
◤ TECHNOLOGY DIFFERENTIATION · 2 / 2
ANTARIKSHA-RAKSHA · 07 / 12
Against the alternatives
Commercial SSA
External warning feeds
ANTARIKSHA-RAKSHA
HOSTING
Cloud services (e.g., LeoLabs)
External government source
Runs locally
DEPLOYMENT
Cloud; free and paid tiers
Email / API delivery
Single laptop · offline-capable
COST
Free and paid tiers (varies)
No fee; access terms apply
₹0 software license cost
AI TRANSPARENCY
Varies by vendor
Not applicable (data feed)
Local open-weights LLM, provenance-labeled
HUMAN CONTROL
Varies
N/A
Human decision required — no command path
RPO / PROXIMITY
Offered by some (e.g., LeoLabs)
Conjunction-focused
Dwell-time detection, intent-neutral
AUDITABILITY
Not assessed
Not assessed
Decision log · CSV · incident reports
Notes: Comparison, stated conservatively and without ranking. Commercial SSA: cloud services such as LeoLabs (subscription service; documents maneuver and RPO detection and AI/ML); free and paid tiers exist (Slingshot Beacon). External warning feeds: the USSPACECOM free conjunction-assessment service, with CDMs posted to Space-Track for account holders and email notifications (Spaceflight Safety Handbook v1.7). Auditability of competitors was not assessed. Our column is what the prototype actually does.

## Slide 8
◤ IMPACT METRICS
ANTARIKSHA-RAKSHA · 08 / 12
Single-run measurements on the demo laptop (2 Oct 2026)
<1 s
PROPAGATE + SCREEN SINGLE RUN · 2 OCT 2026
103
OBJECTS INGESTED FROM CELESTRAK 2 OCT 2026
775
AUTOMATED TESTS PASSED 613 BACKEND + 162 UI · 5 OCT 2026
1
DEMO LAPTOP NO DATACENTER
SINGLE RUNS · DEMO LAPTOP · 2 OCT 2026
103 objects ingested from CelesTrak and 1,012 asset/object pairs screened; propagation + screening < 1 s (0.18 s + 0.16 s, single run). Full refresh 11–35 s across 6 refreshes, network-dependent. 775 automated tests passed (613 backend + 162 frontend, 3 Oct 2026). Risk uses a simplified analytic Pc indicator — not an operational covariance-based Pc. Every decision is made by a human and kept in a persistent audit trail. Runs on one laptop — no datacenter.
SUSTAINABILITY IMPACT
Debris-cascade avoidance is environmental protection of the orbital commons — LEO is a finite resource for future Indian missions. Local inference on one laptop avoids a datacenter footprint.
ECONOMIC IMPACT
Satellites are high-value assets whose navigation, banking and disaster services are hard to price. The prototype has zero software license cost; operational deployment costs are not yet estimated.
Notes: Single-run measurements on the demo laptop on 2 Oct 2026: 103 objects ingested from CelesTrak and 1,012 asset/object pairs screened, 0 real events; propagation + screening under 1 s (0.18 s + 0.16 s); full refresh 11 to 35 s across 6 refreshes, network-dependent; 775 automated tests passed (613 backend + 162 frontend, 3 Oct 2026). Risk is a simplified analytic Pc indicator, not an operational covariance-based Pc. Every decision is made by a human and kept in a persistent audit trail. Sustainability and economic impact are qualitative; operational costs are not yet estimated.

## Slide 9
◤ THEME ALIGNMENT
ANTARIKSHA-RAKSHA · 09 / 12
Sustainable & Resilient India — in orbit and on the ground
RESILIENT
Space is the invisible backbone of payments, navigation, telemedicine, and cyclone warnings. A locally-run decision-support layer keeps working offline after the first data download — cached data, AI fallback, graceful degradation.
SELF-RELIANT BY DESIGN
Built on open-source components and a local open-weight model — no cloud AI, no license fees. Orbital data still comes from CelesTrak today. Designed so whoever deploys it can run and inspect it locally.
SUSTAINABLE
Protecting LEO from debris cascades is sustainability — the orbital environment is a natural resource shared with every future Indian mission. The system itself runs locally on one laptop.
Viksit Bharat 2047 will be a spacefaring economy. This prototype shows a layer it could use — built now, on hardware India already has.
Notes: Theme alignment: Resilient (works offline after the first data download, with fallbacks), Self-reliant by design (built on open-source components and a local open-weight model, no cloud AI, no license fees; designed so whoever deploys it can run and inspect it locally; orbital data still from CelesTrak today), Sustainable (protecting the orbital commons). Close on Viksit Bharat 2047.

## Slide 10
◤ SCALABILITY & ROADMAP
ANTARIKSHA-RAKSHA · 10 / 12
From one laptop to a national capability
PHASE 0
Complete
Working end-to-end prototype: ingest → screen → analytic Pc indicator → local-AI briefs → human decision → audit → alerts. Tested, demo-ready; private repository.
PHASE 1 · 0–6 MO
Harden
Full catalog (30,000+ objects) · standard CDM ingestion · realistic per-object covariance · enterprise identity + MFA · one-command installer.
PHASE 2 · 6–18 MO
Data & AI
Authoritative / indigenous data and sensor fusion, if access is granted · governed evaluation of model adaptation · maneuver-planning research.
PHASE 3 · 18+ MO
Scale nationally
Possible national SSA ops-cell deployment: SQLite → PostgreSQL, horizontal screening workers — planned, not yet built. Partner data-sharing, if agreed.
Scaling paths are planned, not yet built or measured — and the human-in-the-loop governance model stays unchanged.
Notes: Roadmap (planning, not commitments): Phase 0 complete (working, tested prototype with analytic Pc indicator; private repository). Phase 1: full catalog, CDM ingestion, covariance, enterprise identity and MFA (beyond today's prototype RBAC), installer. Phase 2: authoritative/indigenous data and fusion if access is granted, governed model evaluation, maneuver-planning research. Phase 3: possible national ops-cell deployment (a planned scaling path, not yet built or measured).

## Slide 11
◤ COLLABORATIONS
ANTARIKSHA-RAKSHA · 11 / 12
Built on open data, designed for India's space ecosystem
TODAY
Public CelesTrak / NORAD orbital data
The pipeline is demonstrated on open sources — no partner integration exists today; the architecture does not depend on one to run.
ACADEMIA (PROPOSED)
IISc / IIT astrodynamics groups for covariance realism and maneuver optimization — a possible teaching platform for India's future SSA workforce.
ISRO · IS4OM / NETRA (PROPOSED)
A complementary operator-facing decision console that could consume IS4OM / NETRA data in a future deployment; no integration exists today.
DRDO (PROPOSED)
Possible methodology review for asset-protection studies — no engagement exists.
IN-SPACe & PRIVATE (PROPOSED)
Possible screening support for Indian NGEs; commercial SSA sensor providers (e.g. Digantara) as potential data partners. Every new constellation is a potential user.
Notes: Ecosystem: today only public CelesTrak data; no partner integration exists, and nothing is integrated with ISRO, IS4OM, NETRA, DRDO or any government system. Proposed (not agreed) pathways: ISRO IS4OM/NETRA as a possible future data source for a complementary console, a possible DRDO methodology review (no engagement exists), IN-SPACe and private NGEs as potential users or data partners (e.g. Digantara, whose SCOT SSA satellite launched 14 Jan 2025), and IISc/IIT for covariance realism and a possible teaching platform.

## Slide 12
◤ THE ASK · 12 / 12
Space-safety decisions deserve tools that can be run locally and inspected.
ANTARIKSHA-RAKSHA is a working prototype that already runs — SGP4 orbital mechanics, a simplified analytic Pc indicator, transparent local AI and a human decision at every step, on one laptop, with zero software license cost.
Mentorship & pilot
Hardening
Authoritative data
ANTARIKSHA RAKSHA
— 'protection of space' ·
Public submission repository — code available for evaluation
Notes: Close: space-safety decisions deserve tools that can be run locally and inspected. ANTARIKSHA-RAKSHA is a working prototype on one laptop with zero software license cost, using a simplified analytic Pc indicator and a human decision at every step. The code is in a private repository, available for evaluation. The ask: mentorship and pilot evaluation, help with hardening, and access to authoritative data. End on the name: 'protection of space'.